## Slide 1
DEPARTMENT OF INTERNET OF THINGS AND ROBOTICS ENGINEERING (IRE)
UNIVERSITY OF FRONTIER TECHNOLOGY, BANGLADESH (UFTB)
PLADICS
A Lightweight YOLO26n-Based Framework for
River-Surface Plastic Waste Detection and Collection
Course : IRE 300 -Capstone Project
TEAM MEMBER
Mst. Esat Jahan Akhi
ID: 2201022
TEAM MEMBER
Jannatul Ferdushi Ayesha
ID: 2201002
SUPERVISED BY
Suman Saha
Assistant Professor, Dept. of IRE, UFTB

## Slide 2
AGENDA
TABLE OF CONTENTS
01
Introduction
02
Problem & Motivation
03
Objectives
04
Literature Review
05
System Architecture
06
Detection Model & Results
07
Navigation, Collection & IoT
08
Demonstration & Conclusion
PLADICS | River-Surface Plastic Detection & Collection System
Overview
2

## Slide 3
01 · INTRODUCTION
INTRODUCTION
RIVER PLASTIC POLLUTION
Plastic debris entering rivers obstructs waterways, harms aquatic life, and fragments into persistent microplastics.
MANUAL COLLECTION IS COSTLY
Manual inspection and cleanup of river surfaces require significant labor, time, and continuous operational effort.
NEED FOR AUTOMATION
Reflections, glare, vegetation, and water motion make automated river-surface plastic detection genuinely difficult.
PROPOSED SOLUTION — PLADICS
PLADICS (Plastic Detection and Intelligent Collection System) is a Raspberry-Pi-based rover that detects floating plastic with a lightweight YOLO26n model, tracks it with ByteTrack, and autonomously navigates to collect it using a conveyor-belt mechanism — with live IoT monitoring throughout.
Real-time Plastic Detection
Target Tracking (ByteTrack)
Autonomous Navigation
Conveyor-Belt Collection
IoT Telemetry Dashboard
PLADICS | River-Surface Plastic Detection & Collection System
Introduction
3

## Slide 4
02 · PROBLEM & MOTIVATION
MOTIVATION
1
SCALE
1,000+ rivers carry nearly 80% of ocean-bound plastic, making upstream interception highly valuable.
2
LABOR
Continuous manual monitoring and removal of river debris is slow, expensive, and hard to scale.
3
RELIABILITY
Reflections, glare, vegetation, and water texture make plastic detection unreliable with simple vision methods.
4
INTEGRATION
Few systems connect detection with tracking, navigation, physical collection, and monitoring in one workflow.
GOAL
Build a lightweight, reproducible detection-to-collection framework that reliably finds river-surface plastic and physically removes it using a low-cost autonomous rover.
PLADICS | River-Surface Plastic Detection & Collection System
Motivation
4

## Slide 5
03 · OBJECTIVES
OBJECTIVES
1
DATASET & DETECTION
Refine and merge public river-plastic datasets, then train a lightweight YOLO26n detector for real-time single-class plastic detection.
2
MODEL SELECTION
Compare YOLO, compact-CNN, and transformer detectors on accuracy, size, and CPU latency to choose a deployment-ready model.
3
NAVIGATION & COLLECTION
Integrate ByteTrack-based target continuity with rule-based rover navigation and a conveyor-belt collection mechanism.
4
IoT MONITORING
Stream live telemetry — detections, actions, and system health — to an MQTT / Node-RED dashboard for mission logging.
PLADICS | River-Surface Plastic Detection & Collection System
Objectives
5

## Slide 6
04 · RELATED WORK
LITERATURE REVIEW
Research Area
Key Contribution
Lightweight YOLO for Water Surfaces [1]
Compact YOLOv5-based detector reduces computation for water-surface garbage detection.
Multiclass Surface Litter Detection [2]
SS-YOLOv8n targets multiclass floating litter with a lightweight backbone.
Multi-Scale Feature Fusion [3]
YOLOv8-MSS strengthens multi-scale representation for floating-waste detection.
Attention-Enhanced Detection [4]
Improved YOLOv7 adds fusion and attention modules for floating-debris localization.
Tracking-Assisted Detection [5]
YOLOv5 combined with DeepSORT maintains object identity across video frames.
Transformer-Based Detection [6]
RT-DETR-based models use global context for multi-scale floating-waste detection.
Complex-Scene Robustness [7]
Attention-enhanced YOLO variants improve detection under occlusion and clutter.
PLADICS | River-Surface Plastic Detection & Collection System
Literature Review
6

## Slide 7
05 · SYSTEM ARCHITECTURE
SYSTEM ARCHITECTURE — END-TO-END WORKFLOW
1
Camera Input
Pi Camera V2
captures live river-surface frames
2
YOLO26n Detection
Onboard NCNN inference
finds plastic candidates
3
ByteTrack Association
Assigns persistent
track IDs across frames
4
Target Selection
Confidence + area +
alignment scoring
5
Navigation & Collection
Motor + conveyor
actions via GPIO
6
IoT Dashboard
MQTT telemetry to
Node-RED + CSV log
ONBOARD DEPLOYMENT DETAILS
Runs entirely onboard a Raspberry Pi 4 — YOLO26n exported to NCNN format for efficient edge inference.
Frames captured at 640×480 and processed at 416×416 inference resolution for real-time speed.
Rule-based control converts target position and box area into SEARCH / TURN / MOVE / STOP / COLLECT actions.
L298N motor driver handles drive motors; a GPIO relay activates the conveyor belt on a confirmed collection event.
PLADICS | River-Surface Plastic Detection & Collection System
System Architecture
7

## Slide 8
05 · SYSTEM ARCHITECTURE
HARDWARE STACK
Fig. A: Onboard electronics bay of the PLADICS prototype — Raspberry Pi 4, driver board, battery pack, conveyor motor, and camera boom.
Raspberry Pi 4
Onboard compute — runs YOLO26n (NCNN) detection, tracking, and control logic
Pi Camera Module V2
Captures 640×480 live video of the river / test surface
L298N Dual Motor Driver
Drives the left/right DC motors for rover navigation
Conveyor Belt + Relay
GPIO-triggered conveyor lifts detected plastic on board
Li-ion Battery Pack
Powers compute, motors, and conveyor mechanism
Foam & PVC Chassis
Lightweight buoyant frame housing all subsystems
PLADICS | River-Surface Plastic Detection & Collection System
Hardware Stack
8

## Slide 9
06 · DETECTION MODEL
DATASET PREPARATION & MODEL COMPARISON
7,264
refined images
(from 7,759 raw)
175
invalid boxes
removed
7
detectors
compared
Datasets: RiSID (7,356 imgs, 7 rivers) + Riverine Plastic Litter Dataset, merged and cleaned into a single-class “plastic” dataset (70:20:10 split).
Fig. 1: Detection accuracy of lightweight YOLO models on the cleaned single-class dataset (50-epoch benchmark).
PLADICS | River-Surface Plastic Detection & Collection System
Detection Model & Results
9

## Slide 10
06 · DETECTION MODEL
SELECTED MODEL: YOLO26N — FINAL PERFORMANCE
0.919
Precision
0.844
Recall
0.915
mAP@0.5
0.608
mAP@0.5:0.95
2.38M params · 5.2 GFLOPs · 5.13 MB · 7.96 FPS (CPU)
Fig. 2: Confusion matrix of the 100-epoch YOLO26n model on the held-out test set.
WHAT THIS MEANS
727 of 812 true plastic instances were correctly detected on the held-out test set.
Extending training from 50 → 100 epochs raised mAP@0.5 from 0.866 to 0.915.
Remaining errors are mostly missed detections in reflective or cluttered scenes.
The 5.13 MB checkpoint is small enough to run comfortably on a Raspberry Pi 4.
PLADICS | River-Surface Plastic Detection & Collection System
Detection Model & Results
10

## Slide 11
07 · NAVIGATION, COLLECTION & IOT
RULE-BASED NAVIGATION & COLLECTION CONTROL
SEARCH
No confirmed target — rover holds position and keeps scanning
TURN LEFT / RIGHT
Target off-center — steer toward the plastic's horizontal position
MOVE FORWARD
Target centered but still small — approach the target
STOP
Target's bounding-box area exceeds the stop threshold
COLLECT
Same target held stable for 4+ frames — conveyor runs for 5 s
Parameter
Meaning
Value
τacc
Minimum confidence to accept a candidate
0.40
Astop
Bounding-box area that triggers STOP
45,000 px
λL / λR
Left / right navigation-zone boundaries
0.33 / 0.66 × width
Ncol
Stable frames required before collection
4 frames
Tcool / Tconv
Collection cooldown / conveyor run time
5 s / 5 s
PLADICS | River-Surface Plastic Detection & Collection System
Navigation, Collection & IoT
11

## Slide 12
07 · NAVIGATION, COLLECTION & IOT
REAL-TIME IOT MONITORING
Fig. 3: Live PLADICS IoT dashboard — plastic detected, tracked, and collection actively in progress.
MONITORED PARAMETERS
Detection count & confidence
Active ByteTrack ID
Navigation action & mission state
Conveyor ON/OFF status
Inference time & frame rate
CPU / RAM / temperature
Broker: local Mosquitto (MQTT) → Node-RED dashboard. Every mission also writes a timestamped CSV log, and the annotated video stream is served live over Flask MJPEG.
PLADICS | River-Surface Plastic Detection & Collection System
Navigation, Collection & IoT
12

## Slide 13
08 · DEMONSTRATION
SYSTEM DEMONSTRATION
Fig. 4: Assembled PLADICS rover — conveyor ramp, chassis, and onboard electronics bay.
Fig. 5: Live field trial — rover positioned in front of target plastic bottles during a test run.
Fig. 6: Dashboard view during a live run — plastic detected and tracked (Track ID 183, conf. 0.61).
PLADICS | River-Surface Plastic Detection & Collection System
Demonstration
13

## Slide 14
08 · DEMONSTRATION
QUALITATIVE DETECTION RESULTS
Fig. 7: YOLO26n detections on real river-surface test images — varying illumination, background, and object scale.
PLADICS | River-Surface Plastic Detection & Collection System
Demonstration
14

## Slide 15
08 · DEMONSTRATION
RESULTS AT A GLANCE
91.5%
mAP@0.5
(final model)
5.13 MB
checkpoint size
(edge-deployable)
7.96 FPS
CPU inference
throughput
7,264
cleaned training
images
A single lightweight checkpoint powers detection, tracking, navigation, and collection — fully on board a Raspberry Pi 4.
PLADICS | River-Surface Plastic Detection & Collection System
Results
15

## Slide 16
08 · DEMONSTRATION
CONTRIBUTIONS
DATASET
Refined and merged a 7,264-image multi-source river-plastic dataset from RiSID and the Riverine Plastic Litter Dataset.
MODEL
Selected and tuned a lightweight YOLO26n detector achieving 0.915 mAP@0.5 at just 5.13 MB.
INTEGRATION
Combined ByteTrack-based tracking with rule-based navigation and physical conveyor-belt collection.
MONITORING
Built a live MQTT / Node-RED IoT dashboard with mission-level CSV logging and MJPEG streaming.
PLADICS | River-Surface Plastic Detection & Collection System
Contributions
16

## Slide 17
CONCLUSION
CONCLUSION & FUTURE WORK
CONCLUSION
PLADICS demonstrates a complete, working detection-to-collection pipeline: a lightweight YOLO26n model detects river-surface plastic, ByteTrack keeps track of it, rule-based logic drives the rover and triggers the conveyor, and every mission is logged and streamed live to an IoT dashboard.
Proof-of-concept validated on a physical rover prototype
Runs fully on board — no cloud dependency for inference
Detection, tracking, navigation & collection are all integrated
FUTURE WORK
1
LARGER FIELD DATASETS
Collect river-specific data across seasons, cameras, and lighting.
2
OBSTACLE-AWARE NAVIGATION
Add sensing beyond rule-based logic for safer autonomous movement.
3
EXTENDED FIELD TRIALS
Validate long-term autonomous operation on real rivers, not test tanks.
4
MULTI-CLASS SORTING
Separate collected plastic by type using the multiclass detection models.
PLADICS | River-Surface Plastic Detection & Collection System
Conclusion & Future Work
17

## Slide 18
REFERENCES
REFERENCES
[1] L. Chen and J. Zhu, “Water surface garbage detection based on lightweight YOLOv5,” Scientific Reports, vol. 14, no. 6133, 2024.
[2] Z. Fan, Z. Qin, W. Liu, M. Chen, and Z. Qiu, “SS-YOLOv8: A lightweight algorithm for surface litter detection,” Applied Sciences, vol. 14, no. 9283, 2024.
[3] J. Wang and H. Zhao, “Improved YOLOv8 algorithm for water surface object detection,” Sensors, vol. 24, no. 15, p. 5059, 2024.
[4] C. Peng, B. He, W. Xi, and G. Lin, “Improved YOLOv7 algorithm for floating waste detection based on GFPN and long-range attention mechanism,” Wuhan University Journal of Natural Sciences, vol. 29, no. 4, pp. 338–348, 2024.
[5] M. Nunkhaw and H. Miyamoto, “An image analysis of river-floating waste materials by using deep learning techniques,” Water, vol. 16, no. 10, p. 1373, 2024.
[6] B. Sun, H. Tang, L. Gao, K. Bi, and J. Wen, “RTDETR-MARD: A multi-scale adaptive real-time framework for floating waste detection in aquatic environments,” Journal of Marine Science and Engineering, vol. 13, no. 5, p. 996, 2025.
[7] T. Zhou et al., “ESAK-YOLO: Multi-scale attention enhanced object detection for floating waste in complex water scenes,” Scientific Reports, 2026.
[8] M. MacLeod, H. P. H. Arp, M. B. Tekman, and A. Jahnke, “The global threat from plastic pollution,” Science, vol. 373, no. 6550, pp. 61–65, 2021.
[9] L. J. J. Meijer, T. van Emmerik, R. van der Ent, C. Schmidt, and L. Lebreton, “More than 1000 rivers account for 80% of global riverine plastic emissions into the ocean,” Science Advances, vol. 7, no. 18, 2021.
[10] G. Jocher, J. Qiu, M. Liu, S. Lyu, F. C. Akyon, and M. E. Kalfaoglu, “Ultralytics YOLO26: Unified real-time end-to-end vision models,” arXiv:2606.03748, 2026.
PLADICS | River-Surface Plastic Detection & Collection System
References
18

## Slide 19
THANK YOU!!
Questions & Discussion